Solutions to Day3 Hands-On
HighRR SPICE Hands-On 2017, Day 3

---
Noise analysis of the pre-amplifier
Find the a , b and c coefficients
d overline i_n^2 = { {1} over {2%pi} }cdot( 2qI_g + {4kT} over {R_D} ) d%omega
d overline v_{no,i}^2 = d overline i_{n}^2 cdot color magenta {{ {1} over {%omega^2 C_f^2} }}
d overline v_n^2 = { {1} over {2%pi} }cdot( A_T + {A_f} over {%omega{}} ) d%omega
d overline v_{no,v}^2 = d overline v_{n}^2 cdot color magenta {{ (1+ {C_i} over {C_f} )^2 }}
s_o( %omega ) = d overline v_{no,i}^2 + d overline v_{no,v}^2 = ( a^2 + {b^2} over {%omega^2} + {c^2} over {%omega^{}} ) d%omega
color magenta {a^2 = {1} over {2%pi}cdot A_T cdot { (1+ {C_i} over {C_f} )^2 }}
color magenta {c^2 = {1} over {2%pi}cdot A_T cdot { (1+ {C_i} over {C_f} )^2 }}
color magenta {b^2 = { {1} over {2%pi} }cdot( 2qI_g + {4kT} over {R_D} ) cdot {{1} over {C_f^2} }}

---
Noise source in our simulation
- Same configuration
- Current source di2n given the “noise current source”, with PSD
- voltage source dv2n given the “noise voltage source”, with PSD
- Calculation will show that
d overline {i_n^2} = { {1} over {2%pi} }cdot{{4kT} over {R_n}} cdot d%omega
d overline {v_n^2} = { {1} over {2%pi} }cdot{4kTR_n} cdot d%omega
Noise current source
Noise voltage source
a^2 = { {1} over {2%pi} }cdot{4kTR_n} cdot { (1+ {C_i} over {C_f} )^2 }
b^2 = { {1} over {2%pi} }cdot{{4kT} over {R_n}} cdot { {1} over {C_f^2} }
color magenta {%tau_c= {a} over {b} = R_n( C_i+C_f )}

---
Noise simulation of the pre-amplifier
- In file “day3_CSA_Noise”, do the .tran simulation to verify the functionality of this circuit.
- Set Ci = 99pF, Cf = 1pF, do the .noise simulation, find out corner frequency
  - Get “a” value
  - Get “b” value
  - Get tc = a/b
- Sweep the value of Ci in the range of 0~1nF, to see the changes of “a” and “b” noise components in the PSD

---
Noise analysis of CR-RC filter
- Calculate the output noise of CR-RC
  - Input PSD
  - Noise transfer function
  - Output PSD
  - integration
s_i( %omega ) = ( a^2 + {b^2} over {%omega^2} )
H( %omega ) = {V_o( %omega )} over { V_i(%omega) } = color magenta {{j%omega%tau} over {(1+j%omega%tau)^2} }
Useful integration formula
s_o(%omega) = s_i( %omega ) cdot lline H(%omega) rline ^2 = color magenta {( a^2 + {b^2} over {%omega^2} ) cdot { {%omega^2 %tau^2} over {(1+%omega^2 %tau^2)^2} }}
overline {v_n^2} = int from{0} to{%infinite} s_o( %omega ) d%omega

---
Noise simulation of CR-RC filter
- In file “day3_CSA_CRRC_Noise”, do the .tran simulation, for output “out”
  - Maximum value VM and peak time tM
  - Pulse width tW(1%)
- Set Ci = 99pF, Cf = 1pF, do the .noise simulation, get the output noise value
  - Fit with your analysis results?
- Sweep the value of Ci in the range of 0~1nF, plot Vn~Ci
- Sweep the shaping time “ts” in the range of 0.1~10u, plot Vn~ts.
  - Which is the optimized shaping time for CR-RC filter?
  - For the optimized shaping time, calculate SNR (eta)
  - Calculate the inferiority coefficient (F)
%eta_{opt} = {V_M} over {V_n}
F = {%eta_{%infinite}} over {%eta_{opt}}

---
Sweep input capacitance

---
Sweep shaping time constant

---
Comparison of different shaper
- Finish the circuit blocks of “day3_SCA_CRRCx_Noise” (x=2,3,4). Finish the block “day3_ActiveFileter_Noise”
- Set the shaping time for every block at optimum, which is given in lecture. For the active filter, set the shaping time constant the same of CR-(RC)4
- Do .tran simulation, find out the Maximum value VM ,peak time tM and pulse width tW(1%)
- Do .noise simulation, find out the output noise Vn
- Complete the table below
	CR-RC	CR-(RC)2	CR-(RC)3	CR-(RC)4	Active filter
VM
tM
tW(1%)
Vn
F