Testbeam in Hamburg

---
Hardware
- 3 layers(15 channels)
  - Two layers full equipped with seven scintillator tiles and SiPMs(#32,#33)
  - One layer only central channel equipped(#34)
- Interface boards
  - Clock
  - Power supply
- Raspberry
  - Configuration
  - Read data(time, amplitude)
- System
  - Box behind telescope and AHCAL

---
Measurements in General
- Setup and check the MIP response
- Calibrations using the LED
- MIP under different gain scale
- Event validation
- Synchronization between layers
- Efficiency
- Power pulsing
- Synchronized to AHCAL

---
Calibrations: hold delay
- Hold delay
- Ensure ADC always sample at the peak of the input signal
- Scan hold-delay DAC values
- Optimized hold delay setting can apply to the MIP
Global hold delay DAC
delay
ADC Sampled value

---
Calibrations: SiPM gain
- SiPM gain
- Set the SiPM gain to be uniform for all channels
  - tune the SiPM bias DAC
  - Global HV=58V
- Procedures
  1. LED runs → SPS → gain
  2. Gain ~ DAC value
  3. Select the DAC value to get a fixed SiPM gain

---
Calibrations
- Trigger threshold
- Put the threshold level so that the DCR of 5Hz for all channels
  - Tune the trigger threshold DAC(global + local)
- Procedure
  1. DCR scan for different DAC
  2. Set the DAC value
Global threshold = 7
Global threshold = 6
Fine DAC: 0~15
Fine DAC: 0~15

---
Surface scan
- System center align to the beam center
- Changing the location of the system
- HitMap: Number of hit to the sensors
Changing the horizontal position of system

---
Pedestal
- Pedestal: output of the chip when no input signal
- Small dispersion(4 bin) between HG/LG branches
- Very small shift in two pedestal runs → pedestal stable
4 bin
Mean value of pedestal
Noise distributions of pedestal

---
MIP: fixed gain
- Spectrum of MIP(Minimized ionization particle) response
- MIP for different gain scale
  - HG(1:1), single photo spectrum visible
  - About 25 p.e. detected for one MIP in E=2.4GeV
  - HG(1:7), two-three MIPs recognizable in central sensor
25p.e
HG(1:1)
MG(1:7)
LG(1:48)

---
MIP: Auto-gain
- Automatic selection between HG/LG branch
  - For large input signal, switch to LG
  - For small input signal, switch to HG, good noise performance
- Scan the gain selection decision level
- Functional
LG(1:48) / MG(1:7)
LG(1:48) / HG(1:1)

---
Synchronization between layers
- Time information
- Synchronization between the same channel in two layers

---
Time Distributions
- Time interval between two contiguous events
- Beam revolution frequency is 1MHz(td=1us)
- Small modulation: time interval is not the integral times of the TDC counter (Vanish if rebin, → exponential)
1us
After rebinning 16

---
Efficiency
- If two layers have the sync event, the chance for the third layer also has the sync event.
- Scan for different energy/rate

---
Validation
- Event validation for first FIFO level
- Validation: output selection
  - Ideally, only the same channel have significant hits
  - Noise, shower… contributes hits for others channels
  - The central channel get most hits
Chip#33,
enabled channel
Chip#32,
same channel
Chip#32,
others channels
6
6

---
Power pulsing
- Front-end bias switch on/off
  - Functional
  - 5us to start-up and stable
  - No apparent shift to the MIPs
  - Dark count is small(power gating signal sync. to the beam)
~5 us
Front-end output
Power gating
trigger

---
Summary
- One month ago, we got “nothing” for testbeam …
- Both hardware and software …
- Efforts to capture the cosmic MIP in lab but got nothing …
- we finished a long list beyond expectation